# Tactrix OpenPort 2.0 Connection Instructions

Here are the Steps

1) Make sure the Engine is turned off. Turn off all accessories including A/C, lights, wipers etc. (Just a precaution)
2) The OBD Port is located as shown in the Picture below. It is a little bit to the left of the clutch pedal on left hand drive EVO.



3) here's a bottom view picture of the port.



4) Handle the tactrix connector as shown in the picture below, so that the wide side of the connector is towards you (you can also think of it as the bar code facing you)



5) You do not need to be looking at the OBD port to get the connector in. With a little searching, the connector should snap right into place. Remember, if you are forcing the connector fit, you are doing something wrong. 



6) Once the Tactrix adapter is connected, you will need to turn the Key to the "ON" Position. Do not turn on the Engine. At this point, you should see the connector glowing in multiple shades of red, yellow and blue.



7) You can now connect the mini-usb cable to the adapter, and the other end to the PC/Laptop. Software instructions will be made available once the release is made public. I will edit this post to put the addendum.